## Slide 1
Greenhouse climate inspection
House 3, Cedar Row Nursery. A fictional site and report, written as a sample file.
Inspection details
Inspector:
Date:
Roof vents open and close on command
Heater serviced this season
House 3 on the day
House 3 holds three benches of tomato seedlings under a gabled glass roof. The inspection checks that the roof vents, the heater and the two climate sensors keep the house between 16 and 27 degrees Celsius.
Sensor A sits above the middle bench and sensor B near the door. Readings for the week are on page 2; actions are on page 3.
The full sensor log is attached to this PDF as a CSV file, and the technician's notes are pinned to page 3.
Guide to venting:
example.com/greenhouse-venting

## Slide 2
Sensor readings, 21 to 27 October
Sensor A, logged every 10 minutes. Daily minimum and maximum air temperature, mean relative humidity and hours with the roof vents open.
Daily maximum, °C
Day | Min °C | Max °C | Humidity % | Vents open (h)
Tue 21 Oct | 14.8 | 26.1 | 71 | 5.5
Wed 22 Oct | 15.2 | 27.4 | 68 | 6.0
Thu 23 Oct | 13.9 | 24.8 | 74 | 3.5
Fri 24 Oct | 16.1 | 28.3 | 66 | 7.0
Sat 25 Oct | 15.7 | 25.9 | 70 | 5.0
Sun 26 Oct | 14.2 | 23.6 | 77 | 2.5
Mon 27 Oct | 15.0 | 26.7 | 69 | 5.5
The house went over the 27 °C limit on two days, Wednesday and Friday. On both days the vents opened later than the controller schedule says.

## Slide 3
Actions and sign-off
Actions
1. Move sensor B away from the door, where drafts lower its readings.
2. Reset the vent controller to open at 24 °C instead of 26 °C.
3. Service the heater before the first frost and record the date here.
Technician's notes
Notes from the vent controller check are attached to this page as a text file. Open the paperclip icon to read them.
Sign-off
Approved by:
Next inspection: